## Slide 1: Reminder R&D
Hieu Nguyen
Intuitive Machines
July 1, 2016

## Slide 2: Reminder
Overview
  All hardware
  Waterproof
  Stupid cheap
Usage
  Press button and an LED blinks lighting up button
  Blinks for 30 minutes or until pressed again
  Stick around the house, shower, etc.
Misc.
  Battery life should last two years
  Blink frequency as slow as 1 Hz
  Target price <$2 at high quantities
OFF
LED Blink
Reset
PB
PB | 30 minutes

## Slide 3: Components
Transparent silicon rubber button
555 timer
Low power LED
Watch battery
Sticky tape for mounting

## Slide 4: Power Analysis
Requirements:
  2 year battery life
  30 minute continuous runtime
  Small “watch battery” button cell
CR2032 3V 225mAh coin cell ($0.17)
  2 years = 17520 hours
  Max Avg Current = 0.7 * 225 mAh / 17520 hours = ~9 uA

## Slide 5: Solutions
Push button control
30 minute timeout
Blink LED
MCU (ATtiny13a)
555 CMOS timer
General purpose 16-stage timer (daisy chained)
Flip flop
Multivibrator transistor circuit
LM3909 LED flasher
NAND gate multivibrator circuit

## Slide 6: 555 Timer
Low cost vs. power efficiency
30 minute one-shot timer
  T = 1.1 * R [ohms] * C [Farads] seconds
  2 resistors, 2 caps
LED flasher
  T = 1 / (0.7*(RA+2RB)*C)
  F = 1 / (0.693(2R)C Hz [50% duty cycle]
  2 resistors, 2 capacitors

## Slide 7: Discrete Multivibrator
Bistable for storing button input
Monostable for one shot timer
Astable for blinking LED
High freq pulse, divided down with Ripple Counter
NAND gate waveform generator

## Slide 8: LEDs
Our eyes perceive different colors at different brightnesses, even though a light might indicate they are the same. Blue and green LEDs always look brighter than red and yellows for the same given mcd output.
LEDs with lower forward voltage (usually red) can extend battery life (will be operational when battery is at lower voltage)
Low V_f, high mcd, low current, low cost, 360 degree visibility

## Slide 9: BOM
Push button, keyboard transparent switch
Control circuit, Timer
LED
Battery
PCB, PCBA
Enclosure
Mount

## Slide 10: Extensions
Bluetooth connected button
Oil/water mixture, like lava lamp timer
Used for old people with poor memories to verify if they completed a task

## Slide 11: Azoteq Reverse Engineer
JANSPORT
Designator | Part # | Description
CONN |  | Battery holder for 2 CR2016 coin cells
BAT | CR2016 | Coin cell batteries x2 for 6V input
BTN |  | Tactile button
LED |  | White LED
U1 | IQS703 | 6-pin MCU
C1, C2 |  | Bypass capacitors
D1 | KL1 | 
R1 |  | 82.5 ohms
T1…5 |  | Test points

## Slide 12: Azoteq Reverse Engineer
Hacked Sample
Designator | Part # | Description
CONN |  | Battery holder for CR2032 coin cell
BAT | CR2032 | Coin cell battery
BTN |  | Tactile button
C_btn |  | 
LED |  | White LED
U1 |  | 8-pin
R3 |  | 220 ohms
R3.5 |  | 10k ohms
U2 | GG5 | LDO? PIN diodes?
D1 | KL1, BAT54 | Schottky diodes
C1 |  | 
D2 |  | 
T1…5 |  | Test points